## Slide 1
Safaricom Ethiopia
PS Core Network
Name: Uma Shankar

## Slide 2: Agenda
Basic overview of main Network Elements
PS Network Architecture
PS Core call flow : 2G,3G,4G LTE
PS Logical Interfaces
CMM Functional Architecture
CMG Functional Architecture
In next available Training Session ::
APN (Access Point Name) Fundamental Overview.
PS Core KPIs Introduction.
NetAct use to fetch KPIs.
PCRF Functionalities
PS Core Alarms Template to guide AM team

## Slide 3: What is the Core Network?
A core network is a telecommunication network's core part, which offers numerous services to the customers who are interconnected by the access network. Its key function is to direct telephone calls over the public-switched telephone network.

## Slide 4
What is CS Core and PS Core?
Core Network is split into CS domain and PS domain. CS domain is based on original GSM network. PS domain is based on original GPRS network.
CS domain: used to provide Circuit-switched service.
PS domain : used to provide packet switching service.

## Slide 5: What is the PS Core?
PS Core (Packet Switch) is an Access Point Name (APN) is a reference to GGSN where in general, it can be seen as a reference to the Service. According to the APN set on Handset and provisioned in Network, user will get a specific IP Address that is routable to a certain service.

## Slide 6: What is 2G Network?
2G is the second-generation cellular network. The 2G networks are primarily used for the transmission over voice, 2G is the communication technology intended to provide the mobile communication over voice.
2G also called as GERAN.

## Slide 7: What is 3G Network?
3G is the Universal Mobile Telecommunication system (UMTS) is a third-generation (3G) broadband, packet-based transmission of text, digitized voice, video and multimedia at data rates up to 2 megabits per second (Mbps).
3G also called as UTRAN.

## Slide 8: What is 4G Network?
4G LTE (Long Term Evolution )- basically its for PS & LTE is a 4G wireless communication standard developed by the third 3rd Generation Partnership project (3GPP) that's designed to 10x the speed of 3G network for Mobile device such as smartphones ,tablets,netbooks,notebooks and wireless hotspots.
4G also called as EUTRAN.

## Slide 9
Network Elements :-
GERAN-2G-GSM (Global System for Mobile)
UTRAN-3G-UMTS ( Universal Mobile Telecommunication System)
EUTRAN-4G-LTE ( Long Term Evolution)
RNC is 3G . BSC is 2G.
RNC- Radio Network Controller
The Radio Network Controller (RNC) is a governing element in the UMTS radio access network (UTRAN) and is responsible for controlling the Node Bs that are connected to it.

## Slide 10
BSC- Base Station Controller
The Base Station Controller is in control of and supervises a number of Base Transceiver Station(BTS).The BSC is responsible for the allocation of radio resources to a mobile call and for the handovers that are made between base stations under his control.
MSC (Mobile Switching Center)
MSC is a telephone exchange that makes the connection between mobile users within the network, from mobile users to the public switched telephone network and from mobile users to other mobile networks.

## Slide 11
HLR (Home Location Register) – provide Terminal Information
HLR is the main database of permanent subscriber information for a mobile network. The HLR is an integral component of CDMA (code division multiple access),TDMA (time division multiple access), and GSM (Global System for Mobile communications) networks.
VLR ( Visitor Location Register) – provide Terminal Location
VLR is a database that contains information about the subscribers roaming within a mobile switching center’s (MSC) location area.

## Slide 12
SMSC – Short Message Service Center
A Short Message Service Center (SMSC) is a network element in the mobile telephone network. Its purpose is to store, forward, convert and deliver Short Message Service (SMS) messages. The full designation of an SMSC according to 3GPP is Short Message Service - Service Center (SMS-SC).
GMSC (Gateway Mobile Switching Center)
The Gateway Mobile Switching Centre (GMSC) is a special kind of MSC that is used to route calls outside the mobile network. Whenever a call for a mobile subscriber comes from outside the mobile network, or the subscriber wants to make a call to somebody outside the mobile network the call is routed through the GMSC.

## Slide 13
MGW (Media Gateway)
A media gateway is a translation device or service that converts media streams between disparate telecommunications technologies such as POTS, SS7, Next Generation Networks (2G, 2.5G and 3G radio access networks) or private branch exchange (PBX) systems. Media gateways enable multimedia communications across packet networks using transport protocols such as Asynchronous Transfer Mode (ATM) and Internet Protocol (IP).
BTS(Base Transceiver Station)
A base transceiver station (BTS) is a piece of equipment that facilitates wireless communication between user equipment (UE) and a network.

## Slide 14
PSTN – Public Switched Phone Network
PSTN is the aggregate of the world's circuit-switched telephone networks that are operated by national, regional, or local telephony operators, providing infrastructure and services for public telecommunication.
AUC – Authentication Center
AUC is a function in a GSM network used for the authentication a mobile subscriber that wants to be connected to the network. Authentication is done by identification and verification of the validity of the SIM.

## Slide 15
EIR— Equipment Identity Register
EIR is a database that contains a record of the all the mobile stations (MS)that are allowed in a network as well as an database of all equipment that is banned, e.g. because it is lost or stolen.
In the MSC, there are four main elements.
Home Location Register (HLR)
Visitor Location Register (VLR)
Equipment Identity Register (EIR)
Authentication Center (AUC)

## Slide 16
HSS – Home Subscriber Server
The home subscriber server (HSS), or user profile server function (UPSF), is a master user database that supports the IMS network entities that actually handle calls.
Note- HSS and HLR is same in LTE.
MME- Mobility Management Entity
The MME is the key control-node for the LTE access-network. It is responsible for idle mode UE (User Equipment) paging and tagging procedure including retransmissions.

## Slide 17
eNodeB – Evolved Node B
E-UTRAN Node B, also known as Evolved Node B, is the element in E-UTRA of LTE that is the evolution of the element Node B in UTRA of UMTS. It is the hardware that is connected to the mobile phone network that communicates directly wirelessly with mobile handsets, like a base transceiver station in GSM networks.
GPRS core network ( General Packet Radio Service )
The GPRS core network is the central part of the general packet radio service (GPRS) which allows 2G, 3G and WCDMA mobile networks to transmit IP packets to external networks such as the Internet. The GPRS system is an integrated part of the GSM network switching subsystem

## Slide 18
PDN – Public Data Network
PDN is circuit- or packet-switched network that is available to the public and that can transmit data in digital form. A PDN provider is a company that provides access to a PDN and that provides any of X.25, frame relay, or cell relay (ATM) services.
PCRF – Policy and Charging Rules Function
Policy and Charging Rules Function (PCRF) is the software node designated in real-time to determine policy rules in a multimedia network. As a policy tool, the PCRF plays a central role in next-generation networks.

## Slide 19
SGW– Signalling Gateway
A signaling gateway (SGW) is a network component used for sending signaling messages between common channel signaling (CCS) nodes, which communicate with the help of different transports and protocols.
PGW – Packet Data Network Gateway
The PGW acts as the interface between the LTE network and other packet data networks, such as the Internet or SIP-based IMS networks.. The PGW serves as the anchor point for network mobility and: Acts as the Policy and Charging Enforcement Function (PCEF) Manages quality of service (QoS)

## Slide 20: Core 2G,3G Architecture

## Slide 21: GPRS Interfaces

## Slide 22: PMM state machine
PMM-DETACHED
  No communication between MS and SGSN
  SGSN does not hold valid location or routing information for MS
  MS is not reachable by PLMN
  It moves to PMM-CONNECTED through GPRS Attach procedure. PS signaling connection is established between MS and SGSN for performing GPRS Attach.

## Slide 23: PMM state machine (contd)
PMM-CONNECTED
  MS location is known in the SGSN with the accuracy of a serving RNC (Routing Area)
  Location of MS is tracked by serving RNC
  MS performs Routing Area update when RAI changes
  PS signaling connection is established between MS and SGSN
  It moves to PMM-IDLE when PS signaling connection is released due to any reason
  It moves to PMM-DETACHED after GPRS Detach
PMM-IDLE
  MS location is known in the SGSN with the accuracy of Routing Area
  Paging is needed in order to reach MS
  MS and SGSN have established PMM contexts
  MS performs a Routing Area Update if the RA changes
  It enters to PMM-CONNECTED when the PS signaling connection is established between MS and SGSN (e.g. Service Request)
  It moves to PMM-DETACHED after GPRS Detach
  SGSN may perform an “Implicit GPRS detach” after Implicitly Detached timer expires or irrecoverable radio error occurred causing the loss of logical link

## Slide 24: Session Management (SM) State machine
This state machine is present in UE and SGSN
This state machine is valid only when PMM state of the MS is not PMM-DETACHED
Data transfer can happen only when the PDP context is in Active state. So, if the subscriber wants to send or receive data, a PDP context must be activated after attaching to SGSN.
RAB is created at the time of PDP context activation.
RAB is released when PDP context is deactivated
State change
PDP context state moves from “Inactive” to “Active” when PDP context is activated.
PDP context state moves from “Active” to “Inactive”
  When PDP context is deactivated
  MS is detached normally
  MS is detached forcefully when Implicit detach timer expires

## Slide 25: GPRS Attach
The major steps in GPRS Attach procedure are as follows:
MS sends attach request with its identity (P_TMSI) to SGSN
SGSN authenticates MS and then checks whether the user is authorized for the service by checking with HLR
SGSN sends a Attach Accept reply to MS with P-TMSI (TLLI)
A database is maintained in SGSN that maps the mobile identity with TLLI

## Slide 26: GPRS Detach
MS initiated GPRS Detach
To move from READY/STANDBY state to IDLE state, MS initiates GPRS detach procedure by sending Detach request to SGSN
On getting this, SGSN will delete the GMM and PDP contexts for this MS.
SGSN sends Delete PDP context message to GGSN to delete PDP contexts in GGSN
GGSN acknowledges with Delete PDP context response
On getting, SGSN sends Detach accept to MS
MS initiated GPRS Detach
To move from READY/STANDBY state to IDLE state, MS initiates GPRS detach procedure by sending Detach request to SGSN
On getting this, SGSN will delete the GMM and PDP contexts for this MS.
SGSN sends Delete PDP context message to GGSN to delete PDP contexts in GGSN
GGSN acknowledges with Delete PDP context response
On getting, SGSN sends Detach accept to MS
MS initiated GPRS Detach
To move from READY/STANDBY state to IDLE state, MS initiates GPRS detach procedure by sending Detach request to SGSN
On getting this, SGSN will delete the GMM and PDP contexts for this MS.
SGSN sends Delete PDP context message to GGSN to delete PDP contexts in GGSN
GGSN acknowledges with Delete PDP context response
On getting, SGSN sends Detach accept to MS

## Slide 27: Routing Area Update
Routing Area update is done by MS in the following scenarios:
  MS enters new RA
  Periodic RAU timer in MS expires
Intra SGSN RAU
  Old RA and new RA are served by same SGSN
  RA update due to periodic RAU timer expiration is always Intra SGSN RAU
Inter SGSN RAU
  SGSN will accept only those RAU requests with old RA/old SGSN configured as co-operating RA/co-operating SGSN.

## Slide 28: PDP Context Activation
MS initiated PDP context activation
When MS is attached to SGSN, it is assigned a TLLI, which is known in the wireless network. However, the external networks nodes (e.g. server in internet) do not know the MS yet. So, MS must initiate PDP context activation with GGSN:
MS sends a PDP context activation request to SGSN
SGSN chooses the GGSN (that serves a particular type of context) and requests the GGSN to create a context for the MS.
GGSN replies to SGSN with the TID information
SGSN sends a message to MS informing that a context is activated.
MS initiated PDP context activation
When MS is attached to SGSN, it is assigned a TLLI, which is known in the wireless network. However, the external networks nodes (e.g. server in internet) do not know the MS yet. So, MS must initiate PDP context activation with GGSN:
MS sends a PDP context activation request to SGSN
SGSN chooses the GGSN (that serves a particular type of context) and requests the GGSN to create a context for the MS.
GGSN replies to SGSN with the TID information
SGSN sends a message to MS informing that a context is activated.

## Slide 29: MS-initiated PDP Context Deactivation
MS sends a Deactivate PDP Context Request message to the SGSN.
SGSN forwards the request to the GGSN.
GGSN removes the PDP context and returns response.
SGSN returns deactivation complete message to MS.
For WCDMA Systems, the SGSN and RNC exchange information to release the RAB for the PDP context . When the last RAB is released the Iu connection is also released

## Slide 30: Network-initiated PDP Context Deactivation
This happens when : i) Connection to GGSN is lost ii) Delete subscriber data received from HLR
SGSN sends a Delete PDP Context Request message to the GGSN.
GGSN removes the PDP context and returns response message to the SGSN.
If the deactivation is not due to a detach, the SGSN sends a Deactivate PDP Context Request message to the MS.
For WCDMA Systems, if no active Iu connection exists, the connection must be restored through a paging procedure before the message can be sent to the MS. Nevertheless, the RAB will not be established, since the PDP context is under deactivation.
MS removes the PDP context and returns a Deactivate PDP Context Accept message to the SGSN.
For WCDMA Systems, the SGSN and RNC exchange information to release the RAB for the PDP context between the SGSN and the MS.
When the last RAB is released, the Iu connection is also released.

## Slide 31: 3G Direct Tunnel
Interconnects RNC and GGSN user plane directly
SGSN is bypassed from non-roaming payload traffic
Improved Throughput capacity without SGSN node hardware expansion
Reduce 3G payload latency
SGSN can be located without considering payload transmission
delay
Volume charging in SGSN is no longer possible with 3GDT
There will be a small increase ( Maximum to 10%) in CPU load of application Processors (boards handling the signaling) with 100% 3GDT implementation

## Slide 32: 3G DT call flow – Active PDP Context

## Slide 33: EUTRAN/LTE Architecture

## Slide 34: E-UTRAN Attach Procedure (4G Call Flow):- Step-1

## Slide 35: E-UTRAN Attach Procedure:- Step-2

## Slide 36: E-UTRAN Attach Procedure:- Step-3

## Slide 37: Core 2G,3G and 4G Architecture

## Slide 38: GPRS/UMTS Architecture

## Slide 39: EUTRAN/LTE Architecture

## Slide 40: PS Network Architecture : Safaricom Ethiopia

## Slide 41: 1.CMM (SGSN/MME)

## Slide 42: 1.CMG (GGSN/PGW)
Bellow follows the list of CMG logical interfaces used under the current scope of Nokia Cloud Packet Core deployment. For many of these interfaces different transport protocols alternatives may be considered, the table specifies what transport options are implemented in the deployment.

## Slide 43
VNF Components : CMM
CMM VNFCs are organized according to a multi-tier design strategy in which, the load balancing, transaction handling, and database functions are strategically placed in a hierarchy that can scale independently.

## Slide 44: CMM VMs Functionality
CMM VM | Service | Functionality
NECC(Network Element Cluster Controller) | OAM,NTP | • Provides a centralized operation and management unit that provides interfaces between the CMM and the NMS (the NFM-P, NetAct, or third-party NMS). • Supports CMM distributed VNF aspects such as CPPS redundancy mechanism, VM liveness, LI management and charging aggregation. • Supports the interworking of the CMM with the NFM-P (EMS).
PAPS(Packet Processing Service) | 2G,3G Signalling Traffic,2G User Plane Traffic | • Manages UE registration, authentication, and mobility for GPRS subscribers. • Manages 2G/3G UE bearer setup and management. • Terminates the Gb interface, performs packet ciphering/unciphering , and relays 2G user plane data between the radio network and the GGSN/P-GW via the Gn/Gp/S4 user plane interface. • Terminates the Lawful interception interface for the 2G user plane.
IPPS(IP Packet Processing Service) | 3G User Plane Traffic | • 3G user plane packet processing, buffering, and data forwarding functions • Lawful interception for the 3G user plane • Charging and statistics reporting
CPPS (Control Plane Processing Service) | 4G Control Plane Traffic | • Manages UE registration, authentication and mobility for 4G EPC subscribers. • Manages UE bearer setup and management for data and Voice over LTE services. • Provides hybrid state efficient call processing with local cache that increases signaling capacity, reduces database latency, and optimizes compute resources for both DBS and CPPS.
IPDS(IP Director Service) | terminates the external logical interfaces from the external network’s viewpoint. | • Terminates the external logical signaling interfaces from the external network’s viewpoint. • Performs internal and external load balancing. • Implements link management. • Uses in-house high performance SCTP DPDK stack that recovers 100k S1 link failover in less than one second. • Performs stateful assignment and reassignment of UEs to the CPPSs and PAPSs for efficient call processing. • Implements advanced signaling storm and network load/overload controls. • Supports IPv6 and dual stack IPv4/v6.
DBS(Database service) | open database technology for high capacity database solutions. | • Implements the persistent UE Context database designed to meet the high performance and low latency requirements of CMM • Provides performance management statistic concerning the subscriber count and state

## Slide 45: CMG System Structure

## Slide 46: Cloud Mobile Gateway (CMG)
The Nokia Cloud Mobile Gateway (CMG) is deployed as the Virtual SPGW for vEPC solution
intra-VNF redundancy is implemented and the CMG VNF architecture is based on the below VNF Components VNFC a.k.a VMs:
OAM VM: Operations & Maintenance VM, emulates the CPM-A and the CPM-B, managing the vSPGW, performs the ontrol plane functions, routing protocols, management interface (SNMP, Telnet, SSH and CLI) for configuration, KPI-KCI periodic XML report generation and so on. Will have the Cinder volume attached for persistent memory storage of the KPI/KCIs, CDRs, and Logs.
Two OAM-VMs (Emulation of the CPM cards) are implemented for 1:1 redundancy. OAM-A is the Active VM and the OAM-B is the Hot Standby – where all the state is actively checkpointed to allow a transparent SWO in case of active-failure without any service impact

## Slide 47: CMG VMs Functionality
LB-CP VM:
Load Balancer-Control Plane VM, emulates the interface IOMs/Traffic Line cards, and serves as the ingress/egress of control signaling msgs, ipsec and selective re-assembly of the jumbo GTP-U frames on the S1u and the SGi The LB-VM allows for a single IP address for each 3GPP reference point interface towards the other Network elements (MME, eNodeB, SGW, PGW, TWAG, ePDG) The GTP-C control signaling received on the LB-CP is punted to the OAM control plane which provides the user plane load balancing function to select an MG-VM that can anchor the subscriber session. In this deployment LB-VM will not be used for the GTP-U traffic and we shall implement a distributed data plane model, where once an anchor MG is selected for the session, all the subsequent bearer data plane traffic will be directed towards the specific selected MG Two Load Balancer LB-VMs are deployed to aggregate the control plane traffic from multiple pairs of MGs and both operate in Active mode
MG+ VM:
The MG-VM services include 3GPP Call Processing (Control and Data Plane), the Policy and Charging Enforcement function (PCEF), Application Assurance (L7 DPI). The MG-VMs support all 3GPP gateway functions SGW, PGW/GGSN, SAE-GW(S/PGW,GGSN), ePDG and TWAG.
MG+ VM also has the LB-CP component and the External IO user plane component that provides the external network connectivity as well.

## Slide 48: VMG redundancy protection

## Slide 49: Load Balancing of the Subscriber Sessions
An LB/MG-VM that receives the Create Session Request with a GTP TEID = 0, are punted to OAM-VM for control plane processing. The OAM performs the Load Distribution function and selects an anchor MG. The Anchor MG will answer the Initial Create Session Request and set the GTP-U to the Loopback of the selected anchor MG in the Create Session Response. All subsequent GTP- C traffic can continue to be received on any MG and those GTP-C (now incoming with the TEID populated) will be forwarded to the respective anchor MG and all the Data Plane traffic will be sent to the anchor MG as well.

## Slide 50
Thank You!!!